## Slide 1: How We Print Today: Home Computers
Inkjet Printing
Laserjet Printing

## Slide 2: Types of Home Printing
Inkjet and Laserjet printers are the most common types of printers used with home computers.
These printers are only a fraction of the size of commercial presses and work very differently.
How do inkjet and laserjet technologies work?
CT-108.0

## Slide 3: Inkjet Printers
CT-109.0

## Slide 4: Inkjet Printers
Inkjet printers place small droplets of ink onto paper to create an image.
These printers became available in the 1980s.
Limitations:
  Ink can smear before it’s dry
  Ink can be expensive
  Printing is slow
CT-110.0
Notes: Technology TEKS:
123.2 (c)(12) The student identifies the factors that influence the evolution of manufacturing, construction, communication, energy, power, transportation, and bio-related technology.

## Slide 5: Inkjet Printers
The small droplets of ink are 50-60 microns in diameter. That’s smaller than a human hair!
CT-111.0
Notes: A human hair is 70 microns in diameter.
Tehnology TEKS:
123.13 (c)(5) The student describes quality and how it is measured in computer technology.

## Slide 6: Inkjet Printer Components
PRINT HEAD: This contains nozzles that are used to spray drops of ink of various colors to create a photo image.
INK CARTRIDGE: These hold the different colored ink in separate cartridges.
PRINT HEAD STEPPER MOTOR: This motor moves the print head assembly (print head + ink cartridges) back and forth across the paper.
CT-112.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 7: Inkjet Printer Components
BELT: The belt attaches the print head to the print head stepper motor.
CT-113.0

## Slide 8: Two Main Types of Inkjet Printers
Type 1: Thermal bubble or “Bubble Jet”
  Mechanism of action
    create heat, allowing the ink to vaporize.
    This creates a bubble that pushes ink out of the nozzle onto the paper.
Resistors
To see an animation of Bubble Jet technology,
click here.
CT-114.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software

## Slide 9: What is a Resistor?
A resistor is an electrical component designed to limit the flow of current in an electric circuit. This keeps high currents from damaging electronics or lights.
Resistors limit the flow by converting the current’s energy into heat.
CT-115.0
Notes: Printers use film resistors that have carbon or metal film deposited on a thin ceramic rod.
A resistive coating, such as epoxy or silicone, is then spiraled onto the rod. The amount of spiraling applied depends on the amount of resistance needed.
Resistors are labeled with colors that represent properties of the resistor. For more information, visit http://www.doctronics.co.uk/resistor.htm#colour.

## Slide 10: Two Main Types of Inkjet Printers
Type 2: Piezoelectric or “vibrating crystal”
  Mechanism of action
    crystals are at the back of the ink reservoir of each nozzle.
    When the crystal receives an electrical charge, it will vibrate, pushing a small amount of ink out of the nozzle onto the paper.
Piezoelectric
CT-116.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 11: What does piezoelectric mean?
Piezoelectric refers to a type of crystal that becomes electrically charged when it is acted on by a mechanical force.
The opposite occurs when a charge is put into the crystal. The crystal converts the electrical energy into mechanical energy and vibrates.
Quartz is an example of piezoelectric crystals.
CT-117.0
Notes: The crystal can also act an a transducer to convert mechanical energy into electrical energy. Molecules of the crystal align themselves with the direction of a mechanical force, forming an electric dipole. If the crystal is connected to a conductive metal, a current will run through the metal.

## Slide 12: Laser Printers
CT-118.0

## Slide 13: How Laser Printers Work
Laser printers utilize the principle of
.
The main component of laser printers is a revolving drum made of electrically charged, light-sensitive material.
Static electricity
CT-119.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 14: What is static electricity?
Static electricity is when a charge, positive or negative, builds up on an isolated object.
Objects with opposite electric charges will pull towards each other.
Click here to learn how to create static electricity.
CT-120.0
Notes: Good insulators like plastic, cloth, and dry air do not like to lose electrons. But if they do give up electrons, they will have a positive charge. If a conductor such as metal is present, then the negative charges (electrons) move toward the positive charges, forming electrical current.

## Slide 15: Laser Printer
DRUM
  Mechanism of action:
    The drum has a positive electric charge.
    As the drum revolves, the printer shines a laser across the surface to reverse the charge wherever material is to be printed.
    The drum is then coated with a positive toner, a fine powder that sticks only to the negative parts of the drum.
CT-121.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 16: Laser Printer
  Drum, continued:
    After the drum is coated with a positive toner, a piece of paper is given a negative charge.
    The drum then rolls over the paper. The charge of the paper is stronger than the drum, so the paper pulls the toner from the drum to itself.
CT-122.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 17: Laser Printer
FUSER:
  The paper is then passed through the fuser, a pair of heated rollers.
  Mechanism of action:
    After attracting the toner, the paper is heated while the drum is discharged.
    The heated paper causes the toner powder to melt and fuse with the fibers of the paper. The paper is kept from burning by the speed of the roller.
CT-123.0
Notes: Tehnology TEKS:
123.13(6)(A) The student is expected to: describe the properties and characteristics of computer-related hardware and software;

## Slide 18: Summary of Differences
Inkjet Laser
Cost of printer | Inexpensive | Expensive (esp. for color)
Print Quality | Fair | Excellent
Print Speed | Slow | Faster
CT-124.0