## Slide 1: How We Print Today: Commercial Printing

## Slide 2: How is My Book Printed?
Have you ever wondered how companies make your text books, instruction manuals, or novels?
There are actually two types of printing methods that commercial printers use: Offset Printing and Digital Printing.
Let’s take a trip to a printing factory and see how books are printed!
CT-87.0
Notes: Knowledge

## Slide 3: Pen to Paper
Most authors create a manuscript with a computer word processor. But printers want the file converted to an image format, like Adobe PDF.
The image file is printed in one of two ways: either by offset printing or digital printing.
CT-88.0
Notes: Knowledge

## Slide 4: Offset Printing
Offset printing is based on the old technology of lithography.
Lithography literally means “writing with stones.”
This type of printing is based on the fact that water and oil don’t mix.
This is a lithograph of a cathedral drawn by G. Rowe in 1828.
CT-89.0
Notes: Knowledge

## Slide 5: Why doesn’t water mix with oil?
Water is made up of a negatively charged oxygen atom and two positively charged hydrogen atoms. The atoms are held together by strong hydrogen bonds.
Oil is made up of long chains of carbon atoms with hydrogen atoms attached. These molecules do not carry a charge, so they are only held together by weak bonds called van der Waals forces.
H
O
H
vs.
C
H
C
H
H
H
H
H
CT-90.0
Notes: Explain

## Slide 6: Why doesn’t water mix with oil?
For two molecules to bond, they have to break one of their own bonds and form a new bond with the other molecule. For example:
H2O-H2O + Oil-Oil = 2H2O-Oil
In order for a reaction like this to occur, it has to be energetically favorable. In other words, it can’t cost either water or oil too much energy.
CT-91.0
Notes: Explain

## Slide 7: Why doesn’t water mix with oil?
It would cost a lot of energy for two water molecules to break their strong bonds with each other.
Therefore, water bonds with itself and not with oil, and they do not mix.
This is the basis of the chemical principle that “like dissolves like.”
H
O
H
vs.
C
H
C
H
H
H
H
H
CT-92.0
Notes: Explain

## Slide 8: Lithography
In lithography, the image to be printed is drawn or painted on a piece of smooth limestone with a greasy drawing material.
Gum arabic, a water soluble solution, is then applied, sticking only to the non-oily surfaces and sealing it.
CT-93.0

## Slide 9: Lithography
Next, acid is applied to the stone and a chemical reaction occurs, creating a salt layer around the image.
The greasy drawing material is removed, leaving only the salt layer; it is this salt layer which holds the skeleton of the image's original form.
CT-93.0

## Slide 10: Lithography
Next, while the stone is immersed in water, a roller is used to apply an oily ink to the stone.
The water is attracted to the salt layer and adheres to it. The oily ink is repelled by the water and is forced into the cavity left by the previous drawing material.
Lastly, the stone and paper are run through a press, transferring the ink to the paper and off the stone.
CT-94.0

## Slide 11: Offset Printing
Offset printing uses the same principle of water and oil repelling each other.
Offset printing is also similar to lithography because it uses a plate to transfer an image.
However, instead of contacting the paper directly, the plate with an image on it transfers that image onto an intermediate medium, which then transfers the image to a flat piece of paper.
See How it Works!! 
CT-95.0

## Slide 12: How Offset Printing Works
After a graphic or document is completed, a digital file is created by burning a cd or copying to zip files.
An image from the digital file that the author sends to the printer is put on film, just like a camera puts a picture on film.
The image is then transferred from the film onto a plate. The plate can be made of paper, plastic, or metal.
CT-96.0

## Slide 13: How Offset Printing Works
The most common type of plate uses a thin sheet of aluminum coated with a light-sensitive chemical.
When UV light shines onto the plate through the film with the negative image on it, the lit areas harden and the dark areas do not.
The unhardened areas can then be washed away and the image remains.
Negative Film: The image is lit and the rest of the film is dark.
Light-sensitive coating
Aluminum Plate
CT-97.0

## Slide 14: How Offset Printing Works
The plate is then wrapped on a cylinder and as it turns, it comes into contact with ink. The areas where the image has been formed on the plate chemically attract the ink. The blank areas repel the ink.
Metal Plate
Rubber Blanket
Final Paper Output
CT-98.0

## Slide 15: How Offset Printing Works
The inked plate then “offsets” the image to a roller, usually a rubber blanket, which transfers the image to a piece of paper.
The process is then repeated with a new inked plate for each color needed on that piece of paper.
Metal Plate
Rubber Blanket
Final Paper Output
CT-99.0

## Slide 16: Why use a rubber blanket?
The idea was discovered accidentally by Ira Rubel.
When a sheet of paper did not go through his lithographic machine, the stone pressed ink onto a rubber-covered impression cylinder.
Rubber Blanket
CT-100.0

## Slide 17: Why use a rubber blanket?
He then cycled a sheet of paper through the machine and noticed that the image on the back of it, where the rubber pressed against it, was much sharper and clearer than the image made on the front of the paper by the stone.
Ira then decided to make a machine that used this rubber blanket and the first offset press was born.
CT-101.0

## Slide 18
Offset printing is a great technique for large-volume print jobs.
The master plate can be used thousands of times without wearing out. Therefore, the cost to print 100 sheets is close to the cost to print 100,000 sheets. Of course, paper and ink costs will increase.
Though offset printing is great for large print jobs, the initial equipment and set up costs are high.
Why Offset Printing?
CT-102.0

## Slide 19: Digital Printing
Digital printing is also known as electrophotography.
In electrophotography, a concentrated light draws the image to be printed onto a metal drum coated with a photosensitive material. This puts an electric charge on the metal drum in the shape of the image.
The toner particles are electrically charged and are attracted to the parts of the drum that have an electric charge opposite of the toner. (Opposites attract!)
CT-103.0

## Slide 20: Digital Printing
This forms an image made of toner particles on the drum.
The toner particles are then transferred to the paper using heat and pressure.
The entire process of digital printing must be repeated for each color on the page.
CT-104.0

## Slide 21
-- - ---- -
Step 1: The photosensitive layer is charged.
Step 2: The light from the laser changes the charge to zero where there are to be blank spots in the image.
Step 3: The toner is attracted to the charge.
Step 4: Heat and pressure are applied to bond the toner to the paper.
Step 5: Electric charge is removed from the drum.
+ + + + + + + + + + + + + + + + + + +
+ + + + + + + + + + + + + + +
- - - - - - - - - - - - - - -
- - - - - - - - - - - - - - -
Paper
HEAT
+ + + + + + +
How It Works
CT-105.0

## Slide 22: Offset Printing: Pros and Cons
Pros
Best print/picture quality: Has the highest resolution because the particles of ink form a film and adhere easily to fine lines or small spots on paper threads.
Cost effective if you are printing over 2,000 copies of each page.
Cons
Expensive: The major cost comes from the plates needed, although they can be used thousands of times.
It takes a long time to print a book due to creating a plate for each page.
Cannot easily change the pages and fix errors. New plates have to be made.
CT-106.0

## Slide 23: Digital Printing: Pros and Cons
Pros
Cheap: Especially if you are printing less than 2,000 pages.
Fast: It’s easy for a printer to make 600 books every hour (averaging 300 pages per book).
Easy to change pages and fix typos.
Cons
Picture and print quality cannot match offset printing: Toner is a particulate, not a film, so it cannot create dots and fine lines smaller than the toner particle.
CT-107.0