## Slide 1: Nuclear Weapons

## Slide 2: Meltdown vs. Explosion
A nuclear meltdown occurs when the nuclear reactor gets too hot and the uranium pellets begin to melt.
Meltdowns release a lot of heat and some radioactive gas, but most of the radioactivity stays contained.
Notes: Ask students how this is different from nuclear bombs. Why is a nuclear reactor unlikely to product a nuclear-bomb type explosion? Answer: the radioactive material is still kept separated in a reactor, and not enough off it is in the same place to achieve “critical mass” needed to sustain a chain reaction long enough to generate enough energy to blow the whole thing up.

## Slide 3: Meltdown vs. Explosion
Explosions release tons of radioactive material into the environment. They occur if the melted uranium reacts with other materials.
Melted uranium will quickly heat water to make a steam explosion like the one that happened at Chernobyl.
Hydrogen gas, produced from a reaction between uranium and the metal used to protect the rods, can explode when exposed to oxygen.
Notes: Ask students how this is different from nuclear bombs. Why is a nuclear reactor unlikely to product a nuclear-bomb type explosion? Answer: the radioactive material is still kept separated in a reactor, and not enough off it is in the same place to achieve “critical mass” needed to sustain a chain reaction long enough to generate enough energy to blow the whole thing up.

## Slide 4: Atomic Bombs
Atomic bombs, like the ones used in World War II, also use fission.
However, bombs need extremely high fissionable material.
Nuclear reactors only need a small amount of highly fissionable material.
Notes: See notes on previous slide about chain reaction and critical mass.

## Slide 5: Isotopes with High Fissionability
Uranium 235 is used for fission in nuclear reactors.
However, it is difficult to separate U-235 from U-238.
Bombs need close to 100% of the highly fissionable material.
Plutonium, a by-product of uranium fission, is extremely fissionable.
Plutonium can be extracted from used nuclear reactor pellets through reprocessing.

## Slide 6: Why Doesn’t the Plutonium Fizzle Out?
Since Plutonium is highly fissionable, it will begin to decay very quickly.
This would weaken the size of explosion that a bomb could create.
To keep the plutonium from decaying, scientists keep plutonium at sub-critical mass.
A sub-critical mass is the mass at which a substance will not begin a chain reaction of decay.

## Slide 7: Critical Mass
Critical mass is the mass at which a substance will emit enough neutrons during decay that a chain reaction will occur.
Nuclear reactors keep the uranium close to critical mass to keep the chain reaction.
The control rods keep the chain reaction from getting out of control.
Critical Mass
Notes: There is an animation on this page

## Slide 8: Supercritical Mass
Supercritical mass is the mass at which a chain reaction will continue at an exponential rate.
Bombs keep the plutonium at supercritical mass to make the largest explosion possible.
Supercritical Mass
Notes: There is an animation on this page

## Slide 9: Preventing Early Explosion
The mass cannot be supercritical until detonation of the bomb.
The plutonium is separated into subcritical masses in the bomb.
To start the explosion, the two masses are compressed into each other.
P
P
Notes: There is an animation on this slide

## Slide 10: Nuclear Weapons
Hollow Plutonium Sphere
Conventional Explosives
Explosives compress a plutonium sphere into a supercritical mass.

## Slide 11: Nuclear Weapons
Hollow Plutonium Sphere
Conventional Explosives
Polonium-Beryllium Initiator
A polonium-berylium initiator emits a few neutrons.

## Slide 12: Nuclear Weapons
Hollow Plutonium Sphere
Uranium 238
Conventional Explosives
Polonium-Beryllium Initiator
Uranium 238 reflects some of the neutrons and produce others to increase the reaction rate.

## Slide 13: Nuclear Weapons
Hollow Plutonium Sphere
Uranium 238
Conventional Explosives
Polonium-Beryllium Initiator
The massive increase in pressure from the fission reaction creates the explosion.