## Slide 1: Greenhouse Management Math

## Slide 2: Ventilation
Helps to control the greenhouse temperature during all seasons
Importance:
  Reduce mildew and mold
  Reduce harmful bug numbers
  Helps provide an ideal environment for plants to grow in

## Slide 3: Calculating Required Ventilation
Ventilation is measured in Cubic Feet per Minute (CFM) the amount of air moved within a time period
Fans for ventilation will have labeled their provided CFM
Find the Width, Length, and Height(to the tallest point of the greenhouse)
  Multiply Width × Length × Height = A
A = Minimum Required Ventilation for that greenhouse

## Slide 4: Example
Calculate the Ventilation for a greenhouse with the following measurements:
Width × Height × Length
  8 × 14 × 14ft = 1,568 CFM
W
H
S
L
R
H= 5 ft
S= 7 ft
R= 14 ft
W= 8 ft
L= 14 ft
H= Height of Eaves
S= Length of Roof Slope
R= Height to Ridge
W= Width
L= Length

## Slide 5: Temperature Control: Heat
Heating: Prevention of plants getting too cold
  One of the highest expenses
  Depends on:
    The plants being grown
    Geographic location of your greenhouse
      Montana vs. Texas will have different requirements
      Amount of direct sunlight hits the greenhouse
  Ways to Heat:
    Heat coming from central unit in the main building (attached greenhouses only)
    Heat coils, solar panels, or natural sunlight

## Slide 6: Calculating Required Heater Size
Measured in British Thermal Units (BTU)
What you will need to find:
  Total Area of the Structure (NOT including the floor)
  Subtract to solve for the Temperature difference
    Minimum Outside Temperature
      Coldest expected temperature this winter
    Minimum Inside Greenhouse Temperature
      Minimum desired temperature of the greenhouse
  Heat Loss Value
    Covering on the greenhouse that prevents heat loss
Total Area × Temperature Difference= A
A × Heat Loss Value = Final BTU Answer

## Slide 7: Step 1: Calculating the Total Surface Area
H= Height of Eaves
S= Length of Roof Slope
R= Height to Ridge
W= Width
L= Length
Find the Surface Area of the Walls and Roof Slope
  2 × (H +S) × L = A
Find the Surface area of the end walls
  (R+ H) × W= B
Add A + B together
  A + B = Total Surface area
W
H
S
L
R

## Slide 8: Step 1 Example
Area of the Walls and Roof Slope
  2 × (5 + 8) × 14 = A
  2 × (13) × 14
  28 × 13 = 364
Area of End Walls
  (10 + 5) × 7 = B
  15 × 7 = 105
Add A + B
  364 + 105 = 469 Sq Feet
S = 8 ft
R= 10 ft
H = 5 ft
L= 14 ft
W= 7 ft
Remember PEMDAS
W
H
S
L
R
  2 × (H +S) × L = A
  (R+ H) × W= B
  A + B = Total Surface area

## Slide 9: Step 2: Calculating Temperature Difference
Estimate the Lowest Outside Temperature of the winter season
  Example: 40˚F
Estimate the Minimum Temperature Desired Inside the Greenhouse
  Example: 60˚F
Subtract Inside the Greenhouse Temperature - Outside Temperature = A
Example: 60-40 = 20˚

## Slide 10: STOP!
After solving for the total surface area and temperature difference the next step is to multiply them together.
This will make your answer into British Thermal Units (BTU)
Using the numbers from the example
469 sq ft × 20˚F = 9,380 BTU
Total Surface area: 469 sq ft
Temperature difference: 20˚F

## Slide 11: Step 3: Calculate Heat Loss
After solving for BTU’s…
  From Example: 9,380 BTUs
Every Greenhouse should have a covering
Looking at the sheet
  Find your material (that reduces heat loss) and use the number beside it to calculate for value heat loss
Example: if your green house is covered with 4mm twinwall polycardonate you will multiply your BTU’s by .7
  9,380 × .7 = 6,566 BTU
4 mil polyethylene | 1.20 | 4 mm (5/32") twinwall polycarbonate | .70
6 mil polyethylene | 1.15 | 4 mm roof & single poly walls | .95
6 mil poly double layer (inflated) | .70 | 6 mm (1/4") twinwall polycarbonate | .62
11 mil woven polyethylene | 1.05 | 8 mm (5/16") twinwall polycarbonate | .58
3 mm (1/8") glass (single layer) | 1.13 | 10mm (3/8") twinwall polycarbonate | .53
Double layer insulated glass | .45 | 16 mm (5/8") 5 wall polycarbonate | .33
6mm polycarbonate roof & glass walls | .90 | Polycarbonate / fiberglass (single layer) | 1.20
Type of Cover
Amount of heat reduction

## Slide 12: Finished!!!
You have solved for the minimum BTU’s your greenhouse will need
You can pair this number with different heater sizes to see which one will work best

## Slide 13: Practice Problem!:
The minimum outside temperature is 10˚F and the minimum inside temperature is 70˚F. The greenhouse is covered by 6 mil polyethylene which has 1.15 of heat loss.
Calculate the minimum required BTU’s for a greenhouse that is has the following measurements.
H= 4 ft
S= 6 ft
R= 7 ft
L= 10 ft
W= 5 ft
Remember!
H= Height of Eaves
S= Length of Roof Slope
R= Height to Ridge
W= Width
L= Length
Answer:
17,595 BTU

## Slide 14: How To Solve
Find the Surface Area of the Walls and Roof Slope
  2 × (H +S) × L = A
  2 × (4 + 6) × 10 = A
  20 × 10 = 200
Find the Surface area of the end walls
  (R+ H) × W= B
  (7 + 4) × 5 = B
  11 × 5 = 55
Add A + B together
  A + B = Total Surface area
  200 + 55 =
Subtract Temperatures
10˚ = outside temperature
70˚ = greenhouse temperature
70˚ - 10˚ =
Multiply together
255 sq ft × 60˚ =
Multiply BTU’s by Heat Loss
15,300 × 1.15 =
First Step:
Second Step:
Third Step:
Fourth Step:
Measurements:
H= 4 ft
S= 6 ft
R= 7 ft
L= 10 ft
W= 5 ft
Minimum outside temperature: 10˚F
Minimum greenhouse temperature: 70˚F
Heat reduction from covering: 1.15
255 sq ft
60˚
15,300 BTU’s
17,595 BTU

## Slide 15: Benches
What plants are placed on within the greenhouse
Bench height should NEVER be more than 36 inches
  Why?
    Benches should be accessible to individuals of all heights and wheelchair bound individuals
Bench Materials:
  Concrete
  Plastic
  Metal
  Wood
Bench Layout Types:
  Peninsular Layout
  Longitudinal Layout
  Rolling/Non Stationary Bench Layout

## Slide 16: Peninsular Benches
Aisle
Benches
Benches

## Slide 17: Longitudinal Benches
Aisle
Bench
Bench
Bench
Bench
Aisle
Aisle

## Slide 18: Rolling Benches
Benches
Free Space

## Slide 19: Greenhouse Bench Calculations
Benches can be rectangular, circular, or square
How would you calculate for the area of work space?
        Rectangle:
          X = W × H
        Circular:
          X = πr2
        Square:
          X = Side2

## Slide 20: Bench Problem:
Calculate for the following areas:
  Round to the whole number
X = W X H
  X = 30ft
    X = πr2
      X = 50ft
    3. X = Side2
      X = 36ft
10 ft
3 ft
4ft
6ft
1.
2.
3.

## Slide 21: Reference Websites
http://www.greenhousecatalog.com/greenhouse-fan-calculator
http://www.placergreenhouse.com/ventilation.html
http://www.sherrysgreenhouse.com/oldsite/GHheating.html
http://www.littlegreenhouse.com/heat-calc.shtml
http://www.littlegreenhouse.com/fan-calc.shtml